| Vessel Name | Date (12-DEC-2016) | Print name of person completing checklist |
| --- | --- | --- |

Notify port at least 72 hours before arrival (some require 96 hours) to ensure vessel may be received.

| Navigation & Communications |
| --- |
|  | Communicate with port authorities for any local information |
|  | Plan checkpoints so position can be checked with radar, echo sounder or sight / bearing. |
|  | Note congested areas, restricted areas and underlying obstructions |
|  | Document local traffic reporting regulations, checkpoints and radio frequencies for traffic coordination |
|  | If necessary, report security status, number of persons aboard, fuel, water, oil, cargo, passengers, tonnage, destination, owners info, agent info, date of departure of last port call, official numbers and call sign. |
|  | Discuss potential security issues with crew in pre-arrival meeting |
|  | Review all publications and charts for the port |
|  | ISPS compliant ports, vessel security status and previous ten port calls will be required. |
|  | Check bridge electronics, including echo sounder |
|  | Test inter-ship communications, make contact with engine room |
|  | Check running lights and day shapes |
|  | Hoist appropriate flags |
|  | Use radar/ AIS system to calculate safe distances from other vessels using anchorages |
|  | Have a plan for potential wind, current changes |
|  | Verify communications with deck |
|  | Maintain radio watch on port/ safety frequencies |
| Documentation |
|  | All documents for port call to be stamped with ship’s official stamp and signed by the Master |
|  | List of personal items to be signed by the individuals |
|  | Additional documents typically required by the port: |
|  | Crew list | Medical Inventory | Unmanifested cargo |
|  | Ship’s particulars | Declaration of Security | Cargo Nil list |
|  | Ship stores | Previous 10 port calls list | Vaccination list |
|  | Previous Port Clearance Papers | Personal items list for each person aboard |
| Steering and Propulsion |
|  | Test steering gear (SOLAS ChV Reg 26 Pt 1-2) |
|  | Anchor gear in good working order |
|  | Turn on steering system and test rudders and rudder angle indicator |
|  | Once bow thruster is started, rotate the head and test the clutch/ throttle |

| Safety |
| --- |
|  | Check vessel perimeter to ensure mooring lines, cables, straps in position and secured |
|  | Survey gear properly stowed |
|  | Main engine gear boxes working properly |
|  | Secure loose objects on bridge |
| Personnel |
|  | Brief crew so all understand their duties during mooring operations |
|  | Personnel station at positions and in proper PPE |
|  | Advise personnel what to look for and who to notify in case of suspicious activity |
| PILOT |
|  | Complete JSA for vessel to vessel transfer |
|  | Contact approaching pilot and negotiate boarding procedures |
|  | Have vessel crew stand by to assist |
|  | Crewman to escort pilot to bridge |
|  | Ask pilot about any recommended precautions to be taken ashore, security issued in port, local ordinances or curfews |
|  | Crewman to escort pilot off bridge to disembark |

| secured along side |
| --- |
|  | Secure bow thruster and steering |
|  | Notify engineering when ready to secure engines |
|  | Switch radar to stand by |
|  | Secure running lights |
|  | Turn radios to proper channel to monitor communications with port authorities |
|  | Deploy gangway securely with safety net in place |
|  | Post gangway watch with sign in log |
|  | Post additional security as needed |